## Slide 1
GRAY CODE TO BINARY CODE CONVERTER
Presented by :
Yagna priya – 2620090131
Srikari – 2620040009
Akshith Goud – 2620090065
Vishwam – 2620030566
Teja Sai - 2620090141
DDCA PROJECT • 01

## Slide 2
INTRODUCTION
Gray code is a binary numbering system in which two consecutive values differ by only one bit.
Binary code represents numbers using only 0 and 1.
A Gray-to-binary converter changes a Gray-code input into its equivalent binary output.
This project demonstrates the conversion using digital logic gates.
DDCA PROJECT • 02

## Slide 3
PROBLEM STATEMENT & OBJECTIVES
PROBLEM STATEMENT
Gray code is not directly convenient for ordinary binary arithmetic.
A reliable circuit is needed to convert Gray input into binary output.
OBJECTIVES
Design a combinational logic circuit.
Derive the conversion rules using XOR gates.
Verify the output with a truth table and test cases.
DDCA PROJECT • 03

## Slide 4
GRAY CODE VS BINARY CODE
BINARY CODE
GRAY CODE
Decimal | Binary | Gray
0 | 000 | 000
1 | 001 | 001
2 | 010 | 011
3 | 011 | 010
4 | 100 | 110
5 | 101 | 111
6 | 110 | 101
7 | 111 | 100
Key idea: Gray code changes only one bit between adjacent values.
DDCA PROJECT • 04

## Slide 5
CONVERSION RULES
Remember only two rules to convert Gray code into binary.
DDCA PROJECT • 05
RULE 1
Copy the first Gray bit
B3 = G3
Example: if G3 = 1, then B3 = 1.
RULE 2
Use XOR for every next bit
Next binary bit = Previous binary bit XOR Current Gray bit
XOR gives 0 for same inputs and 1 for different inputs.
XOR TABLE
Input A | Input B | Output
0 | 0 | 0
1 | 1 | 0
Different inputs: 0 ⊕ 1 = 1 | 1 ⊕ 0 = 1

## Slide 6
EXAMPLE : CONVERT 1101
DDCA PROJECT • 06
GRAY INPUT (G)
1 1 0 1
BINARY OUTPUT (B)
1
0
0
1
STEP 1
Copy first bit
B3 = 1
STEP 2
1 XOR 1
B2 = 0
STEP 3
0 XOR 0
B1 = 0
STEP 4
0 XOR 1
B0 = 1
FINAL ANSWER: Gray 1101 → Binary 1001
Say: “Copy the first bit, then use XOR step by step.”

## Slide 7
LOGIC CIRCUIT
The first bit goes straight through; the other three bits use XOR gates.
DDCA PROJECT • 07
GRAY INPUTS
G3 = 1
G2 = 1
G1 = 0
G0 = 1
B3 = 1 (copy)
XOR 1
B2 = B3 ⊕ G2
1 ⊕ 1 = 0
B2 = 0
XOR 2
B1 = B2 ⊕ G1
0 ⊕ 0 = 0
B1 = 0
XOR 3
B0 = B1 ⊕ G0
0 ⊕ 1 = 1
B0 = 1
FINAL OUTPUT
B3 B2 B1 B0
1 0 0 1
Binary = 1001
Remember: one direct connection + three XOR gates = a 4-bit Gray-to-binary converter.

## Slide 8
TRUTH TABLE (BIT - EXAMPLE)
Input Gray code and equivalent binary output
Gray G2G1G0 | Binary B2B1B0
000 | 000
001 | 001
011 | 010
010 | 011
110 | 100
111 | 101
101 | 110
100 | 111
DDCA PROJECT • 08

## Slide 9
APPLICATIONS
Rotary and position encoders: Gray code helps reduce errors when reading adjacent positions.
Digital systems: converts Gray-coded data into standard binary for processing.
Communication and control systems: supports reliable interpretation of encoded values.
Digital electronics learning: demonstrates combinational logic and XOR gate use.
DDCA PROJECT • 09

## Slide 10
CONCLUSION
A Gray-to-binary converter transforms Gray-coded input into binary output.
The most significant bit is copied directly.
Each next binary bit is obtained by XORing the previous binary bit with the current Gray bit.
The design is simple, fast, and can be implemented using XOR gates.
DDCA PROJECT • 10